2008 local s1 answers CSN09101

- Files will have the octal code of 551, or in symbolic r-xr-x--x.

- /bin and /usr/bin

- ls –al ~ > ~/file6; ls –l /bin >> ~/file6

- The directory  is “b” and the size cannot be detected from this information..

- When the machine boots it enters runlevel 5. This line indicates that sshd will be started at this level, at priority 55, and that /etc/init.d/sshd will be executed at that time with the parameter “start”.

- He change files in /etc/skel. He would have to edit this and all new user’s “.” files.

- ifconfig eth0 10.2.1.20 netmask 255.255.255.0 broadcast 10.2.1.255
ifconfig eth1 10.1.25.254 netmask 255.255.0.0 broadcast 10.1.255.255
ifconfig eth2 10.3.25.254 netmask 255.255.255.0 broadcast 10.3.25.255

- ip route add 10.1.0.0/16 dev eth0 
ip route add default via 10.1.25.254

- iptables –F FORWARD
iptables –P FORWARD DROP
iptables –A FORWARD –m state --state ESTABLISHED,RELATED –j ACCEPT
iptables –A FORWARD –i eth0 –o eth1 –d 10.1.2.3–j ACCEPT

- state test should be for RELATED,ESTABLISHED, -o should be -i

- tcpdump can capture all traffic on a connected network, enabling the user to capture any type of traffic. Unencrypted traffic may carry privileged information, such as passwords or confidential information.

- Should start with <virtualhost *:80>. DocumentRoot rather than DocumentHome.

- RewriteEngine on
RewriteCond %{HTTP_HOST} !^www.\.test\.com
RewriteRule ^(.*) http://www.test.com$1 [L,R=permanent]

- Forwarding rules need to avoid infinite looping. Putting a \ in front of a name means the forwarding file for that user is ignored during delivery. However, it should have been \andrew not \gordon.

- The url will be rewritten externally to http://www.soc.napier.ac.uk/~gordon/hello.html, as the HOST matches and the URI does not start “/~neil”. The last RewriteRule is not done due to the first rule having the option “L”.

- the command to set passwords is htpasswd not passwd. Required user should be Require user.

- www	A 10.10.10.2
 	MX web
ns1	CNAME tester.com.
web	A 10.10.10.10
 	A 10.10.10.11

- NEW indicates that this is the first packet of a layer 4 network session. Within the whole rule this permits the first packet of a new http request.

- This translates ip numbers to the domain name grussell.org, but the hostname should have ended with a “.”.

- A mask of 255.255.0.0 (a /16) should give a broadcast of 146.176.255.255.